## Slide 1: SPI
(Serial Peripheral Interface)

## Slide 2: SPI Features
synchronous data transfer
Full-duplex
Single Master / multi slave
Serial interface
Multiple slave devices are supported through selection with individual slave select (SS) lines.
It can be used to communicate with a serial peripheral device like external EEPROM or with another microcontroller with an SPI interface

## Slide 3: Advantages of SPI
Higher throughput (Faster)
SPI: 10Mbs – 20Mbs
Simple Receiver Hardware >>> Simple Shift Register
Support Multiple Slaves
Lower power Requirements than I2C.

## Slide 4: Disadvantages of SPI
Requires more Pins
Master must control all communications (Slave doesn’t issue the
transaction).
Separate SS Lines.
No Flow Control (must know slave speed)

## Slide 5: SPI
The SPI bus specifies four logic signals:
  SCLK(SCK,CLK) : Serial Clock (output from master).
  MOSI(SIMO,SDI,DI) : Master Output, Slave Input (output from master).
  MISO(SIMO,SDO,DO) : Master Input, Slave Output (output from slave).
  SS (CS,CE,CEN): Slave Select (active low, output from master).

## Slide 6: How SPI works ?