## Slide 1: Memory Layout

## Slide 2: Memory layout

## Slide 3
.data section
  Initialized Global Variables/ Initialized Static Global Variables/ Initialized Static Local Variables
  Load Location: FLASH
  Run Location: RAM

## Slide 4
.bss section
  Uninitialized Global Variables/ Uninitialized Static Global Variables/ Uninitialized Static Local Variables
  Load Location: Does not exist
  Run Location: RAM

## Slide 5
.rodata section
  Global Const Variables
  Load Location: FLASH
  Run Location: FLASH

## Slide 6: Stack
Section in RAM created at run time to hold local variables(initialized or uninitialized), also hold local const variables